## Slide 1: Literature survey on agile navigation

## Slide 2
Year & Paper | Publication | Training Method | Differentiator | Limitations
2022 – Learning Robust Perceptive Locomotion | Science Robotics (T. Miki et al.) | Teacher–Student (privileged → imitation), PPO, Curriculum + Domain Randomization, Sim-to-Real | First to robustly fuse vision + proprioception; completed 1-hour Alps hike with zero failures | Needs elevation maps, no explicit uncertainty modeling, lacks recovery maneuvers
2024 – ANYmal Parkour | Science Robotics (D. Hoeller et al.) | Hierarchical RL (navigation + locomotion), Unsupervised perception training, Curriculum Learning | First fully learned hierarchical system for parkour navigation; robust 3D reconstruction; achieved 2 m/s | Slow convergence, discrete skill limits generalization, heavy compute cost
2024 – Viability Leads to Emergence of Gait Transitions | Nature Communications (M. Shafiee et al.) | Bio-inspired RL (PPO), Supraspinal drive + CPG, Parallel sim (Isaac Gym + PyBullet) | Introduced viability (fall-avoidance) as universal trigger; emergent trot–pronk for gap crossing | Simplified CPG, viability kernel intractable, pronk risks energy & hardware

## Slide 3
Year & Paper | Publication | Training Method | Differentiator | Limitations
2025 – Parkour in the Wild | ETH Zürich (N. Rudin et al.) | Multi-Expert RL → DAgger distillation → PPO fine-tuning; depth-noise modeling | Foundation locomotion policy distilled from experts; trained end-to-end from raw depth images | RL fine-tuning unstable, over-reliance on knees (hardware stress), weak long-term memory
2025 – RL Locomotion for Resource-Constrained Quadrupeds | ETH Zürich (D. Plozza et al.) | Concurrent training (policy + estimator), Domain Randomization, Noise injection | Works with minimal sensors (stereo + ToF); concurrent estimator-policy learning; 80% success on 22.5 cm steps | Limited to small robots, untested under sensor failure, estimator less precise than VIO